ADIEQ6100EV 10m electrical city bus

## ADIEQ6100EV 10.5m bus 50-60 seats Electrical City Bus

| Size | Overall dimension | 10500x2480x3100 |
| --- | --- | --- |
|  | Wheelbase | 6100 |
|  | Front/Rear suspension | 2250/2230 |
|  | Door width | Front door 830mm , middle door1180mm |
| Weight Parameters | Curb weight | ≤13T |
|  | Max gross weight | 18T, front axle 6T, rear axle 12T |
|  | Max gross weight | 17500kg |
|  | Curb weight | 11500 |
|  | Load weight | 6000kb |
| Seats | Seat capacity | More than 50 |
| Performance Parameters | Top speed | 65-80km/h |
|  | Max grade ability | 25% |
|  | Continuous driving mileage | ≥300km |
|  | Accelerate time | ≤25s(0~50km/h) |
| Electromotor | Rated running speed | 1500rpm |
|  | Rated power | 100Kw |
|  | Rated torque | 635N.m |
|  | Rated volt | 380V |
| Battery | Battery type | Lithium Ferric phosphate battery |
|  | Battery model | 6DFM90 |
|  | Battery number | 132 |
|  | Acceleration performance (0-60km/h)(unload)(s) | 18 |
|  | Fast charging time(h) | 1.5 |
|  | Slow charging time(h) | 5 |
|  | Motor type | AC asynchronous induction motor |
|  | Power: Rated / Peak (kw) | 100/150 |
| Chassis | Chassis structure | Truss structure low entrance chassis frame |
|  | Gearbox | 2 gears |
|  | Front axle | Door type front axle Model A-702.20-3100 Made in Dongfeng |
|  | Rear axle | Double grade main reducer, Harden Gear,main speed ratio 6.43, model 24ETS01-00005 |
|  | Suspension | Front & rear with spring leaf tablet air suspension |
|  | Tire size | 275/70 R22.5 |
|  | Steering system | Power steering,electric- aid pump |
|  | Brake | Driving brake with dual circuit air brake Parking brake with spring brake |

• Application of the motor drive and control, manual operation of electronic control systems to solve large-capacity lithium-ion battery into a set of application technology, high security and electromagnetic compatibility technical problems.

• development and application of a series of key body and chassis electrical technology, the application of lightweight body technology reducing curb weight.

• through the traditional passenger cars and pure electric passenger car production process similarities and differences of the study, the formation of a pure electric vehicle manufacturing process, to achieve a pure electric passenger bus of line with the traditional flexible production.

• The car uses lithium iron phosphate batteries, continuously variable transmission, low-floor, a square one, the assembly of a more comfortable ride air suspension system, the entire vehicle intelligent information control, and beautiful shape.

• driving zero-emission, low noise, no pollution.

• integrated design, the small body mass, 10.5M passenger-carrying space equivalent to 12 meters rear engine of the bus home space, ideal for city use public transportation, can solve the city's pollution and congestion problems.

Payment terms: T/T

Loading port: Shanghai port of China

FOB: US$233,810.00/Unit