ADIYTK6730H CONFIGURATION & PARAMETER LIST

| Size |
| --- |
| Length/Width/Height (mm) | 7280×2150×2910 |
| Interior height (mm) | 1860 |
| Engine |
| Engine model | Yuchai YC4FA130-30 diesel engine（Euro 3） |
| Engine type | Rear mounted，4 cylinders in-line, 4 stroke, turbo-charged, water cooled, BOSCH high pressure common rail system |
| Max.power/rotating speed (kw/r/min) | 95/3200 |
| Max. torque/rotating speed (N.m/r/min) | 340/1600-2400 |
| Displacement（L） | 2.982 |
| Performance |
| Chassis model | ―――― |
| Top speed (km/h) | 115 |
| Axle distance (mm) | 3430 |
| Front overhang / Rear overhang (mm) | 1670/2180 |
| Angle of approach / departure (º) | 12/11 |
| Wheel track(front/rear)（mm） | 1775/1602 |
| Brake distance (v=30km/h fully loaded) | <10m |
| Fuel consumption (on certain condition) | ≤15 |
| Fuel tank capacity(L) | 110 |
| Curb weight（kg） | 7200/5087 |
| Basic Specification |
| Clutch | Single, dry，φ280mm |
| Transmission | 5 forwards manual, soft axle distant control |
| Front axle | Ends fist,Ⅰsection， Drum brake |
| Rear axle | Integral axle housing, single reduction final drive, speed ratio:4.11, Disc brake |
| suspension system | Leaf spring, F2/R2 air suspension is optional |
| Steering system | Chinese integral power steering |
| Braking system | Dual-circuit air brake, drier，energy storage spring parking brake, WABCO ABS with clearance adjust arm |
| Tire | 215/75R17.5 with wheel house |
| Door and door pump | Single leaf，window type，enclosed pneumatic out-swing door with remote |
| Window | Driver’s window and rear windows of both sides are pull-push window, other windows are fully enclosed hardened window, luxury foldable curtain |
| Functional Specification |
| Body | The body of bus is welded by SS400 rectangular steel tube. Stamped parts molding. Monocoque body |
| Seat and accessories | Standard 22+1 seats, 2+1 arrangement, high-back adjustable airline seats, with handle, bag and armrest，safety belt, the seat can be moved horizontally, the driver seat is mechanical shock absorbed seat with three point fixed safety belt |
| Interior trim | Luxury vinyl forming interior trim, flat floor covered with luxury vinyl |
| A/C system | 12KW built-in A/C |
| Heating system | defroster |
| Video and Audio | Hard disk player +1５″ LCD monitor |
| 灯具 Lamp | Integral front lamp, front ceiling height lamp, side mark lamp |
| Others | Automatic engine fire extinguisher, electric clock ，8kg fire extinguisher, tool box, four safety hammers |
| FOB YANTAI | 31,000USD |