ARCTIC CONTAINER VESSEL 108 TEU

- Class notation:

+1A1 / General Cargo Carrier / CONTAINER / PC6 / E0 / TMON / NAUT-AW/

DG-P / BIS / CLEAN / BWM-T / DAT (-35 deg. C)

Translation of notation:

+ 1A1

The ship is built under the supervision of DNV with machinery and equipment found to be in compliance with the rules and requirements.

General Cargo/container carrier

The ship is built for ”lift on/lift off” of cargo in accordance with DNV's relevant rules for such vessels. Furthermore, the ship is equipped and designed for transportation of containers in the hold and on deck.

E0

Periodically unattended machinery space.

PC6

The vessel built according to DNV regulations for sailing in ice, PC6 - Summer/autumn operation in medium first-year ice which may

include old ice inclusions.

The vessels hull built according to DNV Ice Class PC5 - Year-round operation in medium first-year ice which may include old ice inclusions

NAUT-AW

Extended requirements for one-man workstation, grounding avoidance system and automation level.

DG-P

The ship is arranged for carrying dangerous goods in packaged form in partly or fully closed cargo holds. Relevant cargo specified in "Appendix to the classification certificate".

TMON

Tailshaft monitoring

BIS

Built for in water survey.

CLEAN

Requirements for controlling and limiting operational emissions and discharges.

BWM-T

Ballast water management - treatment.

DAT (-35°C)

Design ambient temp.

Additionally:

DPS 0

Dynamic positioning system without redundancy.

The vessels, shall not be delivered with DNV class approval for notation DPS 0 – but meet all and same demands for DPS 0 DNV class notification.

Hence, all Machinery, equipment, materials and performance, shall be according to DPS0 class demands, installed, tested, commissioned, and delivered accordingly.

- Main Particulars:

Length over all	74,20 m

Length b.p.p.	70,01 m

Breadth moulded	15,20 m

Depth to main deck	8,40 m

Design draught	4,00 m

Scantling draught	6,00 m

Speed	12,5 knots

Deadweight	2890 t

Lightship:                             2088,9 t

Complement                         16 persons crew + 12 day passengers

- Endurance

The capacity of all necessary stores and bunkers shall be sufficient to keep

the ship at sea for a minimum of 27 days, and with 2 days spare.

Range at service speed shall be minimum 7,700 nautical miles at service speed (12,5kn)

The calculation is based on:

90% MCR main engine

at service speed of 12.5 knots

Shaft generator connected

300 m³ gas oil

2 days spare

Store of fresh water for at least 12 days for the basic crew, based on consumption of 200 l/d/person.

- Container capacity

Incl. reefer containers	80

- Tank capacities

Fuel oil	324 m3

Fresh water	37 m3

Water ballast	1289 m3

Lubricating oil	14 m3

Miscellaneous oil	30 m3

Miscellaneous water	54 m3

- Propulsion

Main Diesel Engine	1 x 2040 kW (800 RPM), MAN Diesel&Turbo 6L27/38 MDO,

Fuel type	MDO

Fuel consumption	10t/24h (load 90%, with leak consider),

continuous operation, at:

Design draught: 4m

Service speed: 12,5kn

Clean underwater hull

Deep, wide, calm and streamless water

Water temperature +15 deg. C

Spec. gravity  of water 1.025 kg/dm3

Wind force Beaufort 0

Shaft line with propeller	1 x CPP, ø2,6 m , MAN Diesel&Turbo VBS 940 Mk 5,

Bow thruster	1 x 400 kW, Scana Volda CPT 1.25,

Stern thruster	1 x 300 kW, Scana Volda CPT 1.0,

- Generating sets

Main	2 x 480 kW, Scania Nordhavn Genset GASI 16-05,

Emergency/harbour	1 x 217 kW, Scania Nordhavn Genset GASI 09-07,

- Main machinery

Shaft Generator 	MAN Diesel&Turbo, SE 400 LL4

Anchor mooring winches 	Hatlapa, E-Comb.-SD, 40mm K3/80kN

Mooring winches 	Hatlapa, 2 single mooring winches 80 (M1, M2)

Deck cargo cranes	Liebherr, CBW 45/18.6 ST, CBW 25/19.8

Thermal oil heater	Alfa-Laval, Heater H4-TFO-010, Oil Burner Weishaupt L7Z

Steering gear	Rolls Royce SR642 FCP

Cargo hatches	TTS Marine GmbH, Hatch cover nr 1 – 1285-01, Hatch cover nr 2 – 1286-01

Stores/Man-riding crane	Global Davit GmbH Bes.M.T.12/1.8-4.5

Basket for wheelchair	Global Davit GmbH 1950x990, SWL 3kN

Crane for MOB boat&liferaft	Global Davit GmbH RhS.L.S. 18(29)/4.5-20/2.9

MOB work boat (rescueboat)	Hatecke RB600S

Compressors	Sauer&Son, starting air WP33L, service air SC15

Ballast water management	MMC Green Tech. AS, MMC BWMS 300 m3/h

Fresh water treatment	DOE Sp. z o.o. F02 DODO 300

hydrophore plant

Reverse osmosis	Parker Sear Recovery, Java Sea 8 m3 Digital RO System (A500-R723)

Oily bilge water separator	Alfa-Laval, PureBilge 2505, Separator BWPX 307 TGD-71

Switchboards	Remontowa Electric Solutions

Transformers	Elhand, ET35M-160, emergency ET35M-63

UPS	Eltek, Navigation LIPL20142A.003, Automation LIPL20338.401, LIPL20338.402

HVAC	Novenco

- Ship common systems

Optimal Dynamic Trim (ODT)	SAJ Ship Dynamics

Dynamic measuring	SAJ Ship Dynamics

system (DMS)

CCTV	Wiska

Electronic code lock	Garda/Skalmex

Anti-heeling system	Iron pump automatically operated

Integrated ship control	Lyngsoe

system (ISPS)

Reefer container monitoring	Emerson Climate –

system	implemented system of temperature control for reefer containers, that can be carried both inside of cargo holds and on hatch covers

Fire detection system	Elecom Mastertech

Automatic remote sounding	Emerson

system

Radionavigation	SAM Electronic/Lyngsoe

Internal communication	Lyngsoe

Central clock system	SAM Electronic/Lyngsoe

V-SAT system	Furuno

Dynamic positioning system	Lyngsoe

Computer network	Alphatron Marine

- ISCS - Integrated ship control system

Integrated Ship Control (ISCS) handle all processes in the underlying systems.

- A maneuvering system for the propulsion machinery. To secure automatic distribution of loads and overload protection. (May be integrated in the ISCS).

- Power Management System (PMS) with interface to ISCS.

- Maintenance System for planning of maintenance (hour meters connected).

- Failure detection system with remote diagnosis of failures with registration in PMS and underlying systems.

- TV monitoring with interface to ISCS.

- Data logging for monitoring and use in a “Black Box”.

- Electronic control of access.

- Paging system.

- Automatic logging of machine and maneuvering data.

- Other systems

- Accommodation

Crew	15no of berths in 1-man cabins

Day passengers	12 pers. (Passenger Mess/Recreation room + Luggage compartment)

Galley	furnished with Bohnhoff equipment

Dry provision room	furnished with Bohnhoff equipment

Cold provision room	furnished with Bohnhoff equipment

Laundry	furnished with Bohnhoff equipment

Linen store

Crew mess

Duty mess

Treatment room

Ship’s office

Gym

Crew Change room	equipped with heated and ventilated lockers

Accommodation equipment  of Famos Ship Furniture Factory

- Electrial common system

Common standard voltage systems:
400 Volts, 3-phase 50 Hz, AC
230 Volts, 3-phase or 1-phase, 50 Hz, AC
24 Volts DC

- Miscellaneous

- Ballast and bilge system piping outside ER made of GRE,                                    inside ER - CuNiFe.

- Thermal oil system

- Heating system

- Cargo Handling Area - The forward cargo hold area is designed as a Cargo Handling Area with two tweendecks (deck A & B)   installed, and located in the same vertical height as bottom of 9`6 containers (T84 & T86). This for enabling forklift and other cargo handling equipment enter into the containers, when stowed in front of the handling area in T84 & T86. Tanktop (deck C) also is intended to be used for the same purpose. All tweendecks (A,B,C) equipped  with hatches enabling cargo handling independently from the main cargo hold hatches. Tweendecs with total hight/thickness of apx.  one feet, enabling 20 feet (8`6) to be stowed under the closed tweendeck. Cargo cranes are able to deliver and extract pallet cages with apx. 8 pallets, to and from tanktop and tweendecks in this handling area. Flooring protected with special anti-skid coating. The deck from frame 84 and fore enabled  for operation with two axle 4 wheel forklifts.

- Green Passport - inventory of hazardous materials prepared for obtaining certificate

- Hempel coating system –  PSPC (in Ballast tanks) – open decks areas GALVOSIL

- Bunkering station PS & SB

- Fully equipped workshop with hoisting devices

- Fully integrated bridge – Nacos Platinum

- Gangway access control system – camera with motion detection, integrated with alarm system

- Design:

REMONTOWA Marine Design & Consulting Sp. z o.o. (previously Naval Engineering & Design NED Ltd.)

ARCTIC CONTAINER VESSEL 108 TEU