ADI5251GFB 6X4 Anti-roit water cannon vehicle
Payment terms: T/T

Loading port/destination port: any port of China to XXXX

FOB: US$146,200.00/Unit RHD

(Water Cannon truck)

ADI5251GFB type of anti-riot water artillery based on China heavy duty truck chassis, restructuring, while maintaining the excellent performance of the chassis, but also has a complete self-protection and riot control capabilities of a modern society to quell riots in the preferred group not harmful equipment.

一、

Vehicle main configuration and function

1、Anti-riot water cannons: riot control equipment, two water cannons DC (maximum range of 60m), violence can be long-distance disperse violent.

2、
Around the spray system: the body spray equipment around the system, water spray and tear gas solution

3、
Self-extinguishing systems: roof and the vehicle are equipped with self-extinguishing system, which can spray water and foam concentrate.

4、Wrecker Hydraulic shovel: V-type wrecker shovel, to remove the ground can not be removed obstacles.

5、Vehicle for automatic fire extinguishing system: aerosol with a vehicle for a fixed automatic fire extinguishing device

6、Tear gas: with electronic control Combustion Gas tear gas.

7、Poison gas protection mask: 4 sets of military gas masks

8、Glass and lamp protection net: the cab windows and lamps made of galvanized steel vehicle protection, including safety net for the front windshield glass, flip-style activities.

9、
Centralized control system: PLC programmable control, touch screen operation, centralized control and status display.

10、Rear view and radar: Rear view and radar equipped with one machine

11、Alarming device: the vehicle are installed around the vertex color Baoshan cylindrical lights, 300W alarm configuration.

12、Air-conditioning systems: with air-conditioning system.

二、option configuration and function

1、
Bullet-proof armor: Cabin can be optional A (UL-Ⅲ) level ballistic protection.

三、vehicle main technical parameters

| chassis model | ZZ1257M3847AS |
| --- | --- |
| engine model | WD615.87 |
| emission standard | Europe 3 |
| displacement L | 9.726 |
| max power kw(ps)/rpm | 213KW（290HP）/2200 |
| max torque N.m/rpm | 1160/1600 |
| top speed km/h | 102 |
| driving type | 6×4 |
| cab passenger | 2+2 |
| overall dimension L*W*H mm | 9985×2430×3990 |
| wheelbase mm | 3800+1400 |
| wheel tread front/rear mm | 2022/1830 |
| max gross weight kg | 25000 |
| curb weight kg | 14640 |
| water tank capacity m3 | 9 |

四、chassis brief introduction

Heavy-duty truck chassis Sinotruck Group Co., Ltd. of China's latest product, the technical content, comfort and user-friendly design are walking in the forefront of the domestic heavy truck industry. The chassis has the following advantages:

1、
Cab air suspension shock absorber: The original country, the world's top four full-floating air suspension damping device, in any road conditions to achieve the best damping effect.

2、Driving comfort: luxurious driving area, steering wheel-type plastic materials for the car, feel good, forward and backward, up and down regulation. Driving comfort and anti-human evaluation fatigue index for the domestic industry experts to be the highest level, has reached international standards.

4、

Mirrors: Comparative design models based on advanced large mirror, mirror and front right side of the road men endoscopic vision cleared, so the driver complete control of driving conditions.

5、
Heating and air conditioning: the manipulation of electronic control is equipped with air conditioner, car automatic adjust the temperature.

6、

Rollover Stability: the extent permitted by the regulations, widened front and rear axles of the track, effectively improve the vehicle's anti-roll capability.

7、
Two-stage air filtration system: effectively reduces engine wear early, so that the engine overhaul mileage of 80 kilometers, especially for poor working environment.

8、

Power: In the same series of models, choose 213kw engine configurations, powerful.

9、

Transmission: In the same model chassis, select the 9 files ZF transmission with a synchronizer, shift easy to operate, is conducive to the smoothness of the power transfer can effectively improve the power system of life.

10、
Noise: original muffler system so that muffler effect to achieve international top heavy truck standards.

五、Vehicle layout program (as shown):

侧视图

俯视图

Cab interior control layout

六、
The system of classification introduced:

（一）water system

1、Water Cannon: DC Controlled riot water cannon 2 pcs

extreme range：65m

overawe range：40m

Launch mode: continuous jet, jog jet

Launch medium: dye, gas, water

Control mode: Remote Power Control

●
With continuous shooting water cannons shooting water and burst water features, or by launching dye solution can be labeled or gas to disperse the crowd incident distance, its performance in the international industry-leading level.

●
Body of water guns for our company and the development of famous Hydraulic expert, with independent intellectual property rights; the barrel, and gun manufacturers mouth commissioned professional design and production, the key parts are well-known brands. Water cannons were exposed for electroplating the main pieces of polished, sophisticated look.

●
Targets of violence to achieve precision strikes, in the gun barrel is equipped with lights

water cannon 65m water  Knockdown of an empty oil drum within the range of the deterrence

2、Pump: The large flow of domestic high-quality centrifugal pumps, pump body material is high strength aluminum alloy with high speed, high efficiency, small size and light weight.

●
Type: CB18/50, hydraulic working point by the strict test match, absolute guarantee water cannons performance.

●Hydraulic system consists of automotive engine driven by power take off, pump suction tube through the natural water from the ground water to the pitcher.

3、water tank: by the strong anti-corrosion properties of electrolytic plate, wall paint with waterproof marine epoxy zinc-rich coating.

●

Tank divisions within the device, the buffer driving the water before and after the impact.

●
Tank top window of 550 × 550mm, to facilitate entry into tank maintenance operations.

●Tank with the overflow, the exhaust port.

●With electronic water level meter.

●
Equipped with a filter on the tank inlet valve and drain valve.

●Tank filling water: external fire hydrant water.

4、Electromagnetic induction-type level gauge: The company independent development of products, the use of high chromium content in stainless steel. Compared to conventional liquid level gauge for general industrial use, the electromagnetic induction-type level gauge corrosion resistant, high accuracy, response time and good reliability characteristics.

5、Valve: The valve and the installation of enhanced industrial sealing devices and enhanced valve sensor, which enhance the installation of the sealing device to overcome the large flow of dynamic high-pressure seal with the life of the problem when, after the destruction of rigorous test of reliability , the service life of 20,000 times.

6、Proportioner: the proportion of anti-riot water cannon controlled by setting the mixing ratio mixing device to achieve dye, gas and foam agent and the stability of a fixed percentage of the output mixture.

●Proportional controller is in the basis of absorbing domestic and foreign similar products and on the self-developed products, specializing in the production of components, mixing ratio and stable, high sealing performance.

● 
According to actual need riot scene, installed in the control room with remote control device to select the appropriate media, greatly enhancing the effectiveness of anti-riot water cannon and field work handling ability.

7、
Auxiliary valve: high-quality brass or stainless steel products, excellent corrosion resistance, the switch flexible, long after the park will not be catching.

8、。
Auxiliary piping: All pipes are made of industrial stainless steel pipe, welded by polishing after waxing, good corrosion resistance, technology and beautiful.

9、Additives can: equipment cabin installed three volumes are 100L stainless steel tanks, one for device stain, CS tear gas agents and Class B fire fighting foam liquid. Which agents can tear sealed switch is installed automatically, can ensure mixed-volatile liquid does not occur, and the composition of mixed device and can use, such as hybrid solutions to meet different tear gas and other fluids.

10、
Around the spray protection system: the body has eight heads around the set, where necessary, to spray around the protection of the body, can spray water and tear gas solution.

11、Their fire protection system: the roof and chassis were set 12 nozzles can spray themselves with water and foam liquid fire protection. The foam liquid oil Molotov cocktails and firebombs on the performance of fire 7 times for ordinary water.

（二）Anti-riot equipment:

1、Hydraulic wrecker shoveling: front of the vehicle to install V-hydraulic wrecker shovel, clear the ground is not effective in removing obstacles.

●Shoveling for the lightweight design to meet the quality and the removal of obstacles not less than 1000kg.

● Shoveling down the hydraulic power comes from the automobile engine vane pump driven by a manual multi-lift hydraulic valve control.

●Control lever installed in the driving area, manipulated by the driver.

2、汽
Vehicle for automatic fire extinguishing system: the top cover to install the engine in the car 4 car-specific fixed aerosol fire extinguishing devices to enhance vehicle security.

●。
The device has both automatic and semiautomatic control mode, when the temperature reaches 138 ℃ protected areas, or face the fire, the electronic triggering device will automatically open, quickly ejected micron of white smoke-like aerosol solid form, suspended solids, and in the high temperature rapidly decomposed by high temperature heat absorption and a series of chemical reactions, combustion reactions quickly interrupted chains, to achieve efficient fire-fighting purposes.

● 
The device of no residual fire on the car no pollution, no damage, does not destroy the ozone layer, global warming potential is zero, seismic, shock and corrosion resistance can be strong.

3、Tear gas combustion type electric control: before and after the location of the body skirt with four electronically controlled gas burning type of tear gas, which can effectively prevent the rioting crowd close to the body, covering the safety of vehicles left the riot scene.

4、
Gas masks: 4 sets of special gas masks.

5、Glass and lamp protection net: window glass and lamps made of steel mesh protection.

●
Windscreen of the fence as a whole flip, flip up and down by hydraulic control and positioning.

●
The front grille positioning at any angle, in the process of moving will not sink.

●
Vehicles traveling under safe conditions, the care network can be turned upward to the horizontal position to get a better view.

（三）control system

1、
Water cannons console: Each door is equipped with a console water cannons to control the direction and firing water cannons.

●
Console rear seats arranged in front of the cab, so the one controlled by the back staff.

●Emplacement on the console display is set, you can accurately display the rotation of water cannon water cannon position, through the control handle can accurately grasp the launch angle of the water cannon, to ensure that targets for precision strike riots.

●
Also set up a pressure on the console table, you can monitor the water system is working.

2、Centralized control system: the operation of the vehicle all the equipment are electric remote control operation, the control system by Siemens PLC programmable logic controller, touch screen, the relevant control procedures and control components, reliable operation easy and intuitive.

●
Control system uses a modular design, the line clear, rational layout, ease of maintenance.

●Use of process control equipment to achieve all the logical relationship between the Executive, and to cut a large number of relay control, simplified vehicle line, improved vehicle reliability.

●Water tank level and the level of each tank can focus on the LCD screen displayed on the touch, when the tank water level, or a variety of tank position lower than the warning level audible alarm system and displayed on the LCD screen at the touch of a specific Alarm tank.

●
Programmable controller can control the water cannons and other spray system, the various working conditions

●Using the power of PLC programming can also spray water cannons and other changes in the various functions of the system.

（四）Electrical equipment:

1、Rear view and radar: Rear view with OM7200-based and radar-one, 7-inch LCD monitor installed in the dashboard.

2、
Lights: Vehicles are installed around the vertex color Baoshan cylindrical lights.

3、Alarm: 300W split with alarms, can be used for on-site propaganda. Alarm control panel layout in the dashboard, two 150W speakers installed on the cab roof.

五、option equipments

1、

Bullet-proof armor: Cab optional A (UL-Ⅲ)-class ballistic protection, anti-79 micro-washed steel core rounds.

六Accessories with the vehicle

In addition to the vehicle chassis equipped with maintenance tools, water artillery also was equipped with special tools and spare parts for the following:

1, the suction pipe: 4pcs  2m / pc

2, water filter: 1pc

3, the crescent wrench : 1 pc

4, water hose: 1 reel  DN65

5, the fire connecting buckle: 1 set;

6, hydrant wrench: 1pc