ADIEQ5051 6x6 high mobility armored vehicle

Payment terms: T/T 40% deposit, the 60% balance L/C at sight can be accepted after 5% USA Escrow on order

Loading port/destination port: any port of China to

FOB: US$477,870.00/Unit

| Model | ADIEQ5051 6x6 wheeled high mobility armored vehicle |
| --- | --- |
| Overall dimension(mm) | 7225x2914x2160 |
| Wheelbase（mm） | 2350+1350 3050+1130 |
| Tread front/rear（mm） | 2150/1860/1860 |
| Approach angle（°） | 40 |
| Departure angle（°） | 35 |
| Min. ground clearence（mm） | 300 |
| Curb weight（kg） | 14000 |
| Load weight(kg) | 9000 |
| GVW （kg） | 23000 |
| Max. speed（km/h） | 120 |
| Axle number | 3 |
| Leaf spring | 6/6/6 |
| Max. climbing grade（%） | ＞60% |
| Max. driving side slope（%） | 40% |
| Portrait transit angle（°） | 32 |
| Min. swerve diameter（m） | ≯15 |
| Engine | Model | Cummins ISDe200-30 200hp |
|  | Emission standard | Euro 3 |
|  | Engine type | Water-cooled six-cylinder,4 stroke turbocharged and intercooled diesel |
|  | Displacment | 4.5 L |
|  | Max. output | 147kw/2700r/min |
|  | Max. torque | 550N.m/1200~1700r/min |
| Clutch | Single, dry disc, φ395 spring，hydraulic booster, far-distance control |
| Transmission | Manual, six D drive with Synchronizer, one R drive |
| Divided-moved Ware | manual, two position，higher gear ratio1.08，lower gear ratio 1.35 |
| Drive axle | Split Type cast-iron Axle Housing, steel tube semi-axle bushing，universal-joint cross couping with front/rear axle, Differential Lock on front/rear axle |
| Frame | Run-in frame with two slot side carling |
| Suspension | Independent suspension of Front/Rear axle |
| Brake system | Driving arrester: four wheel double-loop air brake, drum arrester, two brake shoes in front, double-loop pump in series, air-pressure control, two air bag brake in front and rear, front dual disc and Parking arrestor rear wheel brake, drum arrester, air-pressure control |
| Steering system | Front wheel turning, gear wheel and hydraulic power assisted steering system |
| Tyre | 12.00R20 |
| Protection performance | Vehicle Resistance Level: Four sides of this vehicle can resist 56 type submachine gun, 7.62mm steel cored warhead shooting. The top and bottom of vehicle can resist 56 type submachine gun with steel cored warhead shooting. The whole vehicle can resist demolition by explosion device on the side and bottom. |
| Driving type | 6x6 off road Left hand driving |
| Air conditioner | With airconditioner |