ADIEQ5103XFB Armored military patrol vehicle

Payment terms: T/T

Loading port/destination port: any port of China to XXXX

FOB: US$196,000.00/Unit

ADIEQ5103XFB

Technical solutions

一、Dongfeng EQ5103XFB anti-riot armored vehicle, using Dongfeng EQ2100WJ Hummer chassis, 6.5mm bullet-proof body, 39mm PC-type bullet-proof glass, equipped with police lights, sirens, color strobe lights, square lights and other police equipment. The car's armor design, strong sense of deterrence, high space utilization, spacious interior, luxurious interior, anti-elasticity can meet the requirements of the Ministry of Public Security GA668-2006 "General Technical Conditions for Police Anti-riot Vehicles" C-level requirements, can resist the last 20 meters Type 95 rifle 87 type 5.8mm ordinary bomb attack; strong power, good maneuverability, strong off-road capability; vehicle four-door 10 window design, practical, is an ideal military and police special anti-riot armored vehicle.

二、Product shape and interior layout

三、Main function description

1、
Bulletproof armor: The vehicle occupant area, fuel tank, water tank, engine compartment C-class bulletproof, bulletproof shooting holes on both sides and tailgate of the vehicle body, can resist 95 type rifle 87 type 5.8mm ordinary bomb attack; bulletproof off-road wheel assembly, tire installation The wheel bullet-proof continuation device can continue after the puncture.

2、
Warning device: color strobe light, square warning light, alarm, speaker, etc.

3、。
Safe Transporter: The interior is spacious and the vehicle is rated for 12 people.

4、。
Air exchange system: It consists of a cooling fan and an overhead air conditioner evaporator, combined with the foam skeleton of the whole vehicle.

5、Fire fighting in the engine compartment: The engine compartment is equipped with automatic fire extinguishing devices to enhance the fire protection of the engine.

6、Others: search lighting, rear view assembly, independent heater, surveillance camera system, electric winch, etc.

四、Product Specifications

| item | Specifications and parameters, right steering wheel, automatic |
| --- | --- |
| （mm) Overall dimension L*W*H | 6610×2450×2490 |
| （mm）wheelbase | 3800 |
| （Kg）G.V.W | 9500 |
| （Kg）curb weight | 8700 |
| engine model | ISDe285 diesel |
| （L）displacement | 6.7 |
| （Kw/rpm）max power | 210/2500 |
| （N.m/rpm） Max toruqe | 970/1500 |
| （Km/h） Top speed | 129 |
| （m) Minimum turning diameter | 18 |
| Wheel tread front/rear | 1878/1870 |
| （mm) Suspension front/rear | 1325/1485 |
| fuel tank capacity L | 150 |
| tire | 315/80R22.5 |
| tire number | 4+1 |
| Seat numbers | 12人(2+1+9) |
| 防弹等级Bulletproof level | GA668 C grade (20m distance against 95 type rifle 5.8mm ordinary bomb shooting) |

五basic configuration

（一）Vehicle structure

1. 
The whole vehicle is bulletproof: the whole vehicle adopts carbon steel square tube to set up the skeleton, and the external welding uses 6.5mm bulletproof skin board. It has high strength, good bending and torsion resistance, and full range of C-class bulletproof. It can resist 95 type rifle 87 type 5.8mm ordinary Bomb attack. For the transitional installation positions such as the door and bullet-proof glass, it is easy to produce the bullet-proof leak position and do not leave the bullet to penetrate the gap.

2． 
Engine compartment: A bullet-proof grille made of bullet-proof plate is installed directly in front of the engine water tank. The structure is designed to ensure the cooling and ventilation of the engine. At the same time, a tortuous passage is provided to prevent not only the frontal injection of the bullet but also the debris. Jump into the engine compartment. On both sides and the top surface of the nacelle, a dark grille capable of dissipating heat and being bulletproof is provided. In order to facilitate engine maintenance and maintenance, a manual air-extension machine cover with a wide body gas spring assist is provided, and the remote control of the nacelle cover in the driving area is opened.

3． Bulletproof glass window: All glass windows of the whole vehicle adopt PC type bulletproof glass assembly, equipped with steel glass frame body and sealing rubber strip, and bolted with the car body, which is very convenient for disassembly and replacement of glass windows without damaging the body coating. Installed.

4． Bulletproof shooting hole: the shooting hole is closed. The outer baffle is made of thickened anti-ballistic plate. The eversion structure, the barrel extension and aiming are unobstructed, which can meet the requirements of 95 rifle shooting; the built-in hinge can prevent violence and smash; The lock is safe and reliable.

5． Fuel tank bulletproof protection: Use a bulletproof plate to make a box-shaped protective cavity covering the periphery and bottom of the fuel tank to prevent the bullet from penetrating the fuel tank and causing fire.

6． Bulletproof tire assembly: Military off-road tires are used. This tire is especially suitable for poor road surface and non-paved road. The tire is equipped with bulletproof support. When the bullet penetrates the outer tire without internal pressure, the vehicle can still be 30~40km. /h speed, continuous driving more than 50Km.

7． Roof Rotating Sunroof: The roof is equipped with a round bullet-proof rotating sunroof, and the sunroof can be rotated freely infinitely. An anti-riot launcher can be installed on the sunroof rotating body with a bracket.

8． Car interior: The occupant area body and the interior interlayer are made of polyurethane foam filling, which makes the whole car have good heat insulation and noise reduction performance; the whole car interior leather soft bag, the interior is light color pneumatic system special light The material interior trim panel, the window soft material interior ring, luxurious and beautiful; the passenger compartment floor is composed of bulletproof steel plate + sound insulation rubber plate + anti-corrosion thick bamboo board + floor covering, and the floor covering can be selected from silica gel plate or pattern aluminum plate. Both are non-slip, abrasion resistant and impact resistant.

9． Seat: The seat is arranged in a 2+1+9 combination, the front and rear driver seats are single seat, the left side is a folding seat, and the driver's seat is back-to-back, and the rear compartment is facing 9 seats. The reversible single seat can be folded and the rear compartment space is released.

10． Handrail: It is divided into the gripper when each door is on the outside of the car, the gripper when riding in the car, the gripper when the door is opened and the folding handle of the ceiling. The ceiling folding handle can be folded and flipped at 90° for the rear seat occupant to grasp, and folding and folding when not in use does not affect the interior space.

11． Stepping up and down the car: Steps are set under each door outside the car to facilitate getting on and off the car. The stepping surface is punched and embossed, and the anti-slip is strong and reliable.

12． Front bumper: large bevel anti-collision shape, can prevent collision and shift obstacles, and is formed by high-strength steel plate welding.

13． Front and rear towing hooks: Two tow hooks are installed in front of and behind the vehicle for self-rescue and rescue other vehicles.

14． Driving lights: headlights: U-shaped fiber optic duct, double-lens lens, headlight assembly with xenon headlights, high light guide, cool fashion, enhance the brightness of headlights at night while preventing dazzling glare . Install the front fog lamp to adapt to the environment of heavy fog and severe air pollution. A riot wire guard net is attached to the headlights and the rear taillights.

15． Special door locks and door hinges: In order to meet the requirements of anti-riot and anti-smashing, all doors are specially designed with double-locked heavy-duty stainless steel precision casting door locks and built-in limit heavy-duty precision casting door hinges.

16． 
Inside the storage compartment: A long storage locker is placed on each side of the rear compartment to accommodate small objects.

17．

Skylight bench: It is arranged in the middle of the car. It is very convenient to adjust the height by electric. When using it, adjust the height of the bench according to the individual height.

（二）Warning system

| composition | Features and specifications | legend |
| --- | --- | --- |
| turret |  |  |
| Alarm | 6 kinds of regular alarm, call and other functions and automatic memory storage Whistle and bass function selection button Conventional whistle and three whistle conversion options Bass and 6 second country delay switching options Programmatically choose storage |  |
| Alarm horn | Power: 150W Sound pressure level: ≥118dB Frequency response range: 200 ~ 5000HZ |  |
| Square warning light | Imported high-brightness LED tube light source High light-transmissive material shade, no leg color Voltage: 12V, power: 5W |  |
| Long police light | Imported high-brightness LED tube light source White transparent material shade The color of the light can be freely matched between red and blue. Built-in 25 standard flash modes |  |

（三）Audio and video system

| composition | Features and specifications | 图例legend |
| --- | --- | --- |
| Flying song audio and video machine | Digital HD, DVD full-screen touch operation; Play a variety of audio and video media playback formats such as DVD/VCD/CD/MP3/WMA/MPEG4; Support U disk playback, ipod access; Built-in FM/AM radio tuner |  |
| GPS卫星导航 GPS satellite navigation | Full screen smart touch, support for handwriting input Full voice navigation prompt Latest Kay LiDE map Positioning error <10m National fixed speed alarm (fixed electronic dog) |  |
| Reverse image | S SF-9880C camera CCD plus night vision, waterproof, shockproof System: PAL Pixel: 628x582 Angle: 120° Video output: 1.0Vp-p, 75Ω Dimensions: 75x58x78mm CCD plus night vision, waterproof, shockproof |  |

（四）Glare search light

The roof is equipped with SJH135T Xenon glare search light, power 35W, effective illumination distance of 140m, wireless remote control lamp head switch and rotation within 50m, horizontal rotation without dead angle, can rotate within 380°, up and down 100° swing.

（五）Air conditioning and ventilation system

1. Driving area air conditioning: The air outlet is located on the front and bottom of the instrument panel, and the cold and warm air are converted by the knob.

2. Air conditioning in the passenger compartment: the cold air is an independent 4000 air conditioner air conditioner evaporator, and the air outlet is located at the rear of the inner top. The warm air is also a stand-alone heater, and the air outlet is arranged under the seat, which greatly improves the comfort of the warm air inside the cabin.

3. Ventilation system: An electric inlet and exhaust fan is arranged on the roof and the rear of the car for forced exchange of indoor air.

（六）Power system

1. 
Main power switch: When the vehicle is parked for a long time, it is set to prevent leakage of the battery, electromagnetic type 180A.

2. Inverter power supply: Installed in the cabinet, XP-1.0KVA/24V Anderson pure sine wave inverter, input voltage DC24V, output rated power: 1000VA, output voltage AC220V.

（七）Fire extinguishing system

1. Extinguishing dry powder cans: Place 2 fire extinguishing agents on the front side of the second row of seats to deal with sudden fires in case of emergency.

2. Automatic fire extinguishing system: Two car-specific fixed aerosol automatic fire extinguishing devices are installed in the engine compartment of the car to enhance the safety protection of the whole vehicle. When the temperature of the protection zone reaches 138 ° C or an open flame is encountered, the electronic trigger device will automatically turn on, and the aerosol spray can achieve the purpose of high-efficiency fire extinguishing. The device has no pollution to the car and no damage.

六、Camera monitoring system

| composition | Features and specifications |
| --- | --- |
| PTZ camera | Effective pixels: 1920 (H) × 1080 (V); Minimum illumination: 0.1Lux@F1.2; Focal length: f=8~128mm; Zoom factor: Auto zoom 2 megapixel lens, 20x optical zoom, F1.6~2.3; Control mode: RS485, built-in 16 protocols; Network protocol: TCP/IP, UDP, FTP and other protocols; Horizontal angle: 360° infinity; Up and down angle: +40°~-90°; Protection level: IP66; Power: DC9V~DC30V (3.5A car) |
| DVR | Hard disk 1T; video output: 1 channel PAL/NTSC, aviation interface (1.0VP-P, 75Ω) composite video signal output 1 channel VGA output 1 channel HDMI output; image compression: H.264, dual stream; image resolution: PAL/NTSC; Real-time monitoring: 1080P, 720P, 4CIF; Hard disk: Hold 2 hard disks, each hard disk supports up to 1T, and the total storage capacity is up to 2T; Backup storage: U disk, mobile hard disk; Power supply: DC+6V~+36V adaptive, negative ground. The built-in power supply can output up to 140W of power. The built-in power supply has a super capacitor, which can provide about 4 seconds of working power for the device in case of external power failure; Power consumption: 17W (excluding peripherals such as hard disk); Anti-vibration: patented anti-vibration technology; Size: width × depth × height = 180mm × 208mm × 100mm |
| Control Keyboard | Model: Micro Knight VNT-K100 controls the pan/tilt, lens, preset position, patrol queue, track scan, menu setting and other functions of the intelligent camera. |
| Ceiling display | Model: SF-12581080P, 11.4-inch screen System: P system / N system brightness: 300cd / m2 contrast ratio: 300:1 |

七、other

Appearance color and logo: painted according to the police appearance standard system, the paint color of the vehicle is special police blue, and the police emblem and police characters are posted on the front and sides.