Steyr 6x6 off road special vehicle

Payment terms: T/T,down payment 40% arrange for manufacturing,the 60% cash before delivery(or 70% balance L/C at sight can be accepted)

Delivey time: depends on customer order quantity.

Loading port/destination port: Any port of China to XXXX
FOB: US$47,760.00/Unit

Steyr 6x6 off road special vehicle specification

| Steyr 6x6 off road special vehicle (long cargo box) |
| --- |
| Driving type | 6x6 off road for military |
| Overall Dimension (L*W*H) mm | 9915x2480x3350 |
| Cargo box Dimension (L*W*H) mm | 7220x2368x620(long cargo box) |
| Wheelbase (mm) | 4325+1350 |
| Curb weight (kg) | 11650 |
| Front overhang/Rear overhang (mm) | 1576/3030 |
| Front /Rear track (mm) | 1939/1800 |
| Approach angle/Departure angle | 21/17 |
| Max speed (km/h) | 80 |
| Cab | Hydraulic shock absorb adjustable seat, adjustable steering. Safety belt, cabin front protection, cooler protection, light protection, upward exhaust pipe. |
| Engine | Model | WD615.50 WEICHAI DIESEL ENGINE |
|  | Feature | MAN EVB tech. Diesel, 4-stroke direct injection, 6 cylinder in line, radiator, turbo-charging. |
|  | Bore /stroke (mm) | 126x130 |
|  | Displacement (L) | 9.726 |
|  | Power | 290hp/213kw |
|  | Rated speed (r/min) | 2000 |
|  | Torque (N.m) | 1160 |
|  | Emission | EuroII |
| transmission | Model | FAST gearbox |
|  | Shift mode | Manual 9 forward 1 reverse |
|  | Torque (N.m) | 1350 |
|  | First shift ratio | 7.285 |
| Electrical | Battery | 12V/135Ah |
|  | Generator | 28V-35A |
|  | Starter | 5.4Kw/24V |
| Spring leaf | Type | Spring leaf |
|  | Front | 9 |
|  | Rear | 9+6 |
| Axle load weight(T) | Front | 6.5t Steering axle |
|  | Rear | 13t Double reduction, hub redactor driving |
| Steering | Left hand drive Power steering |
| Tire | 14.00-20 military tyre 6+1 spare |
| Clutch | 430 Diaphragm type, single dry frictional disc, hydralic boosting |
| Fuel tank | 380L steel tank |
| Air conditioner | With A/C |