ADIEQ2100E6D 6x6 off road truck

Payment terms: T/T

Loading port: Shanghai port of China

FOB: US$32,000.00/Unit

ADIEQ2100E6D Diesel 6x6 Off-road Truck

| Model | ADIEQ2100E6D Off-road army Truck |  |  |
| --- | --- | --- | --- |
| （kg） Weight Parameter (kg) | Load weight | Off-road travel | 3500 |
|  |  | Highway travel | 5000 |
|  | Max gross weight of traction | 4500 |
|  | Empty load | Front axle load | 2850 |  |
|  |  | Middle、Rear axle load | 3440 |  |
|  |  | Max gross weight | 6290 |  |
|  | Load weight | Front ax;e load | 3265 |  |
|  |  | Middle、Rear axle load | 6725 |  |
|  |  | Max gross weight | 9990 |  |
| Performance parameter | Engine model | 6BT5.9 /EQB160-20 diesel engine |
|  | Engine type | Four-stroke, water-cooled, inline 6-cylinder, supercharged, diesel engines |
|  | Engine power | 118kw 160 horse power |
|  | Gearbox | Manual 5 speed |
|  | Top speed (km/h) | 85 |
|  | Minimum turnning diameter (m) | 18.6 |
|  | (%) Max gradeability (load 3500kg、no traction) | 60 |
|  | Per 100km fuel consumption (L) | 30 |
|  | Brake distance (full load 30km/h) (m) | ≯9 |
|  | Manual brake performance (%) | 40 |
| （mm） Dimension parameter (mm) | Total length | 6996 |  |
|  | Total width | 2400 |
|  | Height (empty load by calash) | 3302 |
|  | Wheelbase | Front axle to the center of the rear suspension | 4025 |
|  |  | Between middle to rear alxe | 1250 |
|  | Wheel tread | Front axle | 1876 |
|  |  | Middle、rear axle | 1870 |
|  | Sidewall inner dimension | Length | 4000 |
|  |  | Width | 2180 |
|  |  | Height | 900 |
|  | Angle of trim | Approach angle | 34° |  |
|  |  | Departure angle | 45° |
|  | Max wading depth | 900 |
|  | Minimum clearance distance between ground | 305 |
|  | After the trailer hook from the pitch (full load) | 857 |
|  | Truck floor height (empty load) | 1400 |