DETAIL PRODUCT :

1TX CR028WIFIKIT

The ready-to-use solution for regulating the temperature in your home directly from your smartphone.

The kit includes the 1TX CR028WIFI chronothermostat and the 1TX RX01WIFI Smartbox.

1TX CR028WIFI

Wi-Fi Chronothermostat

- Wireless connection to Smartbox

- Equipped with backlit LCD display with "White-LED" technology

- All-glass" finish for a pleasant and modern design

- Easily programmable via APP available for both Android and iOS

- Weekly programming

- 3V battery power supply

- Connects directly to the boiler

TECHNICAL FEATURES

- Power supply: 3V-2x1.5V AA (alkaline)

- Display: 4.3" backlit LCD

- Operation: ON/OFF or modulating

- Differential: adjustable 0.2-0.4-0.8-1.6°C with ON/OFF operation

- Control period 10/15/20/25 minutes with modulating operation

- Temperature levels: Up to 10 temperature levels per day

- Temperature: 0.5°C adjustable accuracy

- Control: summer/winter

- Minimum intervention programming 1 minute

- Transmission: 868 MHz RF

- PCB antenna: integrated

- Programmable interventions up to 10 per day

- AWAY function with temperature reduction from 0 to 5°C from the set temperature

SPECIAL NOTES

Anti-limescale operation with pump control

Low Battery signalling

1TX RX01WIFI

Smartbox

- Connected via Ethernet to router

- No configuration required

- Does not require a computer

- Powered by micro USB adapter

- Manages data collected from various connected devices

- Connected to the cloud sends data, downloads weather information and messages

- Each household requires one Smartbox

TECHNICAL FEATURES

- External power supply 5V 500 mA

- Power consumption: 300 mA

- Connection: RJ45 for Ethernet

- LED indications

- Transmission: 868 MHz RF

- PCB antenna: integrated