2009 ATR-72-500

## STRUCTURAL CONFIGURATION

WEIGHT DATA

|  | KG | LB |
| --- | --- | --- |
| MAXIMUM TAXI WEIGHT | 22,670 | 49,978 |
| MAXIMUM TAKE OFF WEIGHT | 22,500 | 49,604 |
| MAXIMUM LANDING WEIGHT | 22,350 | 49,273 |
| MAXIMUM ZERO FUEL WEIGHT | 20,500 | 45,194 |
| OPERATING EMPTY WEIGHT | 13,366 | 29,467 |
| MAXIMUM PAYLOAD | 7,650 | 16,865 |

FUEL TANK

|  | L | US Gal |
| --- | --- | --- |
| LH WING | 3,185 | 1,683 |
| RH WING | 3,185 | 1,683 |
| TOTAL | 6,370 | 3,366 |

ENGINE THRUST RATING	lbf

|  | ESHP | SHP |
| --- | --- | --- |
| MAX. TAKE-OFF | 2,880 | 2,750 |
| NORMAL TAKE-OFF | 2,593 | 2,475 |
| MAX. CONTINUOUS | 2,619 | 2,500 |
| MAX. CLIMB | 2,299 | 2,192 |
| MAX. CRUISE | 2,237 | 2,132 |

| AIRCRAFT MODEL : | ATR72-212A | ENGINE : | PW127M |
| --- | --- | --- | --- |
| REGISTRY : | RP-C7256 | PROPELLER : | 568F |
| MSN : | 847 | AIRCRAFT FH SINCE NEW : | 21537:04 |
| DATE MANUFACTURED : | 30-JAN-2009 | AIRCRAFT FC SINCE NEW : | 26684 |
| AGE : | 13.92 YRS | DATE AS OF : | 31-Dec-22 |

CHECK (LAST DONE)

| CHECK | LAST ACCOMPLISHMENT | MPD INTERVAL | NEXT ACCOMPLISHMENT | REMAINING |
| --- | --- | --- | --- | --- |
|  | FH | DATE | FH | MO | FH | DATE | FH | MO |
| C01 CHECK | 17831:31 | 30−Jun−16 | 8000 | − | 25831:31 |  | 4294 |  |
| C02 CHECK | 17831:31 | 30−Jun−16 | 16000 | − | 33831:31 |  | 12294 |  |
| C03 CHECK | 13218:04 | 26−Jun−14 | 24000 | − | 37218:04 |  | 15681 |  |
| C04 CHECK | 17831:31 | 30−Jun−16 | 32000 | − | 49831:31 |  | 28294 |  |
| 1YE | − | 01−Apr−22 | − | 12 | − | 01−Apr−23 | − | 3 |
| 2YE | − | 27−Sep−22 | − | 24 | − | 27−Sep−24 | − | 21 |
| 4YE | − | 28−Dec−20 | − | 48 | − | 28−Dec−24 | − | 24 |
| 8YE | − | 30−Jun−16 | − | 96 | − | 30−Jun−24 | − | 18 |
| 12YE | − | 28−Dec−20 | − | 144 | − | 28−Dec−32 | − | 122 |

|  | DATE | FH | FC | MRO | VENUE |
| --- | --- | --- | --- | --- | --- |
| WEIGHT & BALANCE | 26−Apr−21 | 21517:40 | 26680 | DORNIER TECH | PHILIPPINES |
| COMPASS SWING | 28−Dec−20 | 21513:45 | 26677 | DORNIER TECH | PHILIPPINES |

| AIRCRAFT MODEL : | ATR72-212A | ENGINE : | PW127M |
| --- | --- | --- | --- |
| REGISTRY : | RP-C7256 | PROPELLER : | 568F |
| MSN : | 847 | AIRCRAFT FH SINCE NEW : | 21537:04 |
| DATE MANUFACTURED : | 30-JAN-2009 | AIRCRAFT FC SINCE NEW : | 26684 |
| AGE : | 13.92 YRS | DATE AS OF : | 31-Dec-22 |

SYSTEM CONFIGURATION

| AUTOLAND | CAT I |
| --- | --- |
| ACARS | N/A |
| FUEL QTY UNIT | Kg |
| RVSM | N/A |
| COCKPIT DOOR | Y |
| COCKPIT DOOR SURVEILLANCE SYSTEM | N/A |
| ADS-B OUT | N/A |
| RNP | 1, APCH |
| RNAV | 1, 2, 5 |
| TCAS VERSION | 7.1 |
| IPRAM | Modifiable |
| EFB | Class I / Type B |
| RADIO ALTITUDE CALLOUT | Y |
| LOW FREQUENCY - ULB (8.8Khz) | N/A |
| HF | N/A |

| AIRCRAFT MODEL : | ATR72-212A | ENGINE : | PW127M |
| --- | --- | --- | --- |
| REGISTRY : | RP-C7256 | PROPELLER : | 568F |
| MSN : | 847 | AIRCRAFT FH SINCE NEW : | 21537:04 |
| DATE MANUFACTURED : | 30-JAN-2009 | AIRCRAFT FC SINCE NEW : | 26684 |
| AGE : | 13.92 YRS | DATE AS OF : | 31-Dec-22 |

CABIN CONFIGURATION

PASSENGER SEAT	GALLEY

ORIGINAL

FLOORING

CURRENT

| OEM | SICMA |
| --- | --- |
| SERIES | 9636200 |
| CLASS | Y |
| QUANTITY | 72 |
| HIC | No |

CABIN ATTENDANT SEATS

| AIRCRAFT MODEL : | ATR72-212A | ENGINE : | PW127M |
| --- | --- | --- | --- |
| REGISTRY : | RP-C7256 | PROPELLER : | 568F |
| MSN : | 847 | AIRCRAFT FH SINCE NEW : | 21537:04 |
| DATE MANUFACTURED : | 30-JAN-2009 | AIRCRAFT FC SINCE NEW : | 26684 |
| AGE : | 13.92 YRS | DATE AS OF : | 31-Dec-22 |

CURRENT FITTED LANING GEAR

### OEM	MESSIER BUGATTI SA

LSV	30-OCT-2014 DATE INSTALLED	08-NOV-2014

MAIN LANDING GEAR

| PN | D23189000-23 |
| --- | --- |
| SN | MN418 |
| POS | LH |

MAIN LANDING GEAR

| PN | D23190000-23 |
| --- | --- |
| SN | MN418 |
| POS | RH |

NOSE LANDING GEAR

| PN | D22698500-6 |
| --- | --- |
| SN | B580 |

| AIRCRAFT MODEL : | ATR72-212A |  | ENGINE : | PW127M |
| --- | --- | --- | --- | --- |
| REGISTRY : | RP-C7256 |  | PROPELLER : | 568F |
| MSN : | 847 |  | AIRCRAFT FH SINCE NEW : | 21537:04 |
| DATE MANUFACTURED : | 30-JAN-2009 |  | AIRCRAFT FC SINCE NEW : | 26684 |
| AGE : | 13.92 YRS |  | DATE AS OF : | 31-Dec-22 |
| FITTED ENGINE |  | DATE AS OF: | 31-Dec-2022 |  |
| ENGINE 1 (LEFT HAND) STATUS INSTALLED |  |  |  |  |

## ENGINE 1 LLPS

| DESCRIPTION | PN | SN | FC LIFE LIMIT | CSI | FC TO GO | FORECAST |
| --- | --- | --- | --- | --- | --- | --- |
| LP IMPELLER | 3072764-01 | EAAD000K046 | 15,000 | 8034 | 6966 | N/A |
| HP IMPELLER | 3072766-01 | A0039BT1 | 15,000 | 10786 | 4214 | N/A |
| HP FRONT COVER | 3039640 | A003EDCX | 15,000 | 8696 | 6304 | N/A |
| HP REAR COVER | 3039639 | A0038XME | 15,000 | 10524 | 4476 | N/A |
| HP DISK | 3041511 | A0038K4L | 15,000 | 10536 | 4464 | N/A |
| LP DISK | 3039412 | A003E84A | 15,000 | 7907 | 7093 | N/A |
| 1ST PT DISK | 3038513 | A002H696 | 30,000 | 23046 | 6954 | N/A |
| 2ND PT DISK | 3033914 | A002FT9Y | 30,000 | 23046 | 6954 | N/A |
| AIR SEAL | 3039172 | UAAE060 | 15,000 | 9280 | 5720 | N/A |

| AIRCRAFT MODEL : | ATR72-212A | ENGINE : | PW127M |
| --- | --- | --- | --- |
| REGISTRY : | RP-C7256 | PROPELLER : | 568F |
| MSN : | 847 | AIRCRAFT FH SINCE NEW : | 21537:04 |
| DATE MANUFACTURED : | 30-JAN-2009 | AIRCRAFT FC SINCE NEW : | 26684 |
| AGE : | 13.92 YRS | DATE AS OF : | 31-Dec-22 |

ENGINE 1 HUB, ACTUATOR, BLADE

| DESCRIPTION | PN | SN | FH LIFE LIMIT | TSI | FH TO GO | FORECAST |
| --- | --- | --- | --- | --- | --- | --- |
| ADJUSTING NUT | 814754-1 | 2T575-2397 | 10,500 | 1218 | 9282 | N/A |
| PROPELLER HUB | 815470-2 | 288 | 10,500 | 1218 | 9282 | SEP2024 |
| PROPELLER ACTUATOR | 815585-7 | 20080923 | 10,500 | 1218 | 9282 | N/A |
| TUBE-TRANSFER | 815587-1 | 970414 | 12,100 | 1218 | 10882 | N/A |
| PROPELLER BLADE | R815505S3W | FR200803070RT | 10,500 | 0 | 10500 | JUL2029 |
| PROPELLER BLADE | R815505-6 | FR2016120036RT | 10,500 | 23 | 10477 | MAR2024 |
| PROPELLER BLADE | R815505-6 | FR200706158RT | 10,500 | 958 | 9542 | OCT2024 |
| PROPELLER BLADE | R815505-6 | FR2017120030RT | 10,500 | 2038 | 8462 | SEP2029 |
| PROPELLER BLADE | R815505R3W | FR807 | 10,500 | 1137 | 9363 | SEP2024 |
| PROPELLER BLADE | R815505R3W | FR20020572RT | 10,500 | 2037 | 8463 | MAR2025 |

CSI	CYCLES SINCE INSTALLED LSV LAST SHOP VISIT

## FITTED ENGINE

ENGINE 2 (RIGHT HAND) STATUS	INSTALLED

| PN | 3073453-01 |
| --- | --- |
| SN | PCE-ED0348 |
| POS | RH |

TECHNICAL SPECIFICATIONS

| AIRCRAFT MODEL : | ATR72-212A | ENGINE : | PW127M |
| --- | --- | --- | --- |
| REGISTRY : | RP-C7256 | PROPELLER : | 568F |
| MSN : | 847 | AIRCRAFT FH SINCE NEW : | 21537:04 |
| DATE MANUFACTURED : | 30-JAN-2009 | AIRCRAFT FC SINCE NEW : | 26684 |
| AGE : | 13.92 YRS | DATE AS OF : | 31-Dec-22 |

ENGINE 2 LLPS

| DESCRIPTION | PN | SN | FC LIFE LIMIT | CSI | FC TO GO | FORECAST |
| --- | --- | --- | --- | --- | --- | --- |
| LP IMPELLER | 3072764-01 | A003HCBM | 15,000 | 7450 | 7550 | N/A |
| HP IMPELLER | 3072766-01 | A003KL00 | 15,000 | 7450 | 7550 | N/A |
| HP FRONT COVER | 3039640 | A003L92B | 15,000 | 8476 | 6524 | N/A |
| HP REAR COVER | 3039639 | A003L8Y7 | 15,000 | 7383 | 7617 | N/A |
| HP DISK | 3041511 | A003KYFT | 15,000 | 7383 | 7617 | N/A |
| LP DISK | 3039412 | A003HH0F | 15,000 | 7721 | 7279 | N/A |
| 1ST PT DISK | 3038513 | A002FCTY | 15,000 | 22400 | 7600 | N/A |
| 2ND PT DISK | 3033914 | A002FLHM | 30,000 | 22400 | 7600 | N/A |
| AIR SEAL | 3039172 | UAAF182 | 30,000 | 9240 | 5760 | N/A |

ENGINE 2 HUB, ACTUATOR, BLADE

| DESCRIPTION | PN | SN | FH LIFE LIMIT | TSI | FH TO GO | FORECAST |
| --- | --- | --- | --- | --- | --- | --- |
| ADJUSTING NUT | 814754-1 | 1012 | 10,500 | 1218 | 9282 | N/A |
| PROPELLER HUB | 815470-2 | 2011090224 | 10,500 | 1218 | 9282 | SEP2024 |
| PROPELLER ACTUATOR | 815585-7 | 20080621 | 10,500 | 1218 | 9282 | N/A |
| TUBE-TRANSFER | 815587-1 | 20070616 | 12,100 | 11239 | 861 | N/A |
| PROPELLER BLADE | R815505-6 | FR201004051RT | 10,500 | 2728 | 7772 | MAY2024 |
| PROPELLER BLADE | R815505-6 | FR20060556RT | 10,500 | 23 | 10477 | JUL2029 |
| PROPELLER BLADE | R815505-6 | FR2016120035RT | 10,500 | 958 | 9542 | FEB2024 |
| PROPELLER BLADE | R815505-6 | FR201605057RT | 10,500 | 2038 | 8462 | JUL2029 |
| PROPELLER BLADE | R815505-6 | FR2017030101RT | 10,500 | 1137 | 9363 | APR2024 |
| PROPELLER BLADE | R815505-6 | FR201604129RT | 10,500 | 2037 | 8463 | JUL2029 |

CSI	CYCLES SINCE INSTALLED LSV LAST SHOP VI

# Text boxes

1

QUANTITY

Rear Right Galley

DESCRIPTION

SIMAIR

OEM

| OEM | SICMA |
| --- | --- |
| SERIES | 9636200 |
| CLASS | Y |
| QUANTITY | 72 |
| HIC | No |

NTF

CURRENT

Carpet

ORIGINAL

1 FWD + 1 AFT

QUANTITY

SICMA

OEM

31-Dec-2022

DATE AS OF:

|  | FH | FC |
| --- | --- | --- |
| SINCE NEW | 22158:00 | 26909 |
| DURING LSV | N/A | 17456 |
| SINCE INSTALLED | N/A | 9453 |
| TO GO | OCT 2023 | 10547 |

|  | FH | FC |
| --- | --- | --- |
| SINCE NEW | 22158:00 | 26909 |
| DURING LSV | N/A | 17456 |
| SINCE INSTALLED | N/A | 9453 |
| TO GO | OCT 2023 | 10547 |

|  | FH | FC |
| --- | --- | --- |
| SINCE NEW | 23541:26 | 28159 |
| DURING LSV | N/A | 17317 |
| SINCE INSTALLED | N/A | 7 |
| TO GO | MAR 2023 | 9158 |

| PN | 3073453-01 |
| --- | --- |
| SN | PCE-ED0071 |
| POS | LH |

|  | FH | FC |
| --- | --- | --- |
| SINCE NEW | 18518:11 | 23792 |
| SINCE LAST HSI | 1858:52 | 2416 |
| TO GO HSI | N/A | N/A |
| NEXT DUE HSI | N/A |
| SINCE LAST OH | 8285:42 | 10182 |
| TO GO OH | N/A | 1144 |
| NEXT DUE OH | N/A |
| DATE INSTALLED | 28-Dec-2020 |

31-Dec-2022

DATE AS OF:

31-Dec-2022

DATE AS OF:

|  | FH | FC |
| --- | --- | --- |
| SINCE NEW | 14735:19 | 17470 |
| SINCE LAST HSI | 859:14 | 944 |
| TO GO HSI | N/A | N/A |
| NEXT DUE HSI | N/A |
| SINCE LAST OH | 859:14 | 944 |
| TO GO OH | N/A | 2953 |
| NEXT DUE OH | N/A |
| DATE INSTALLED | 28-Dec-20 |

31-Dec-2022

DATE AS OF: